## Slide 1
JUICE: a European mission to Jupiter
and its icy moons
JUICE artist impression (Credits ESA, AOES)

## Slide 2: JUICE
Speaker
Date

## Slide 6
Jupiter Icy Moons Explorer
Notes: 6

## Slide 13
Jupiter atmosphere
Atmospheric structure, composition and dynamics
Coupling between troposphere, stratosphere and thermosphere

## Slide 14
Jupiter magnetosphere
Magnetosphere as a fast rotator
Magnetosphere as a giant particle accelerator
Interaction of the Jovian magnetosphere with the moons
Moons as sources and sinks of magnetospheric plasma

## Slide 16
Jovian magnetosphere
Notes: Jovian magnetosphere - The largest object which we can reach to study plasma processes
Fast rotator and powerfull accelerator of charged particles
Interaction of the magnetospheres of Jupiter and Ganymede
Interactions of the material injected by the moons with magnetosphere and upper atmosphere of the giant (aurorae)
Various wave processes

## Slide 18
Elements of the JUICE Program
ESA Ground
Stations
Launcher:
Ariane 5 ECA
Spacecraft: PI provided Airbus D&S instruments
VLBI
Mission Operation Centre (ESOC)
Science Operation Centre
(ESAC)
Science Community
Notes: 18

## Slide 19: JUICE Model Payload
JUICE Payload
JANUS: Visible Camera System PI: Pasquale Palumbo, Parthenope University, Italy. Co-PI: Ralf Jaumann, DLR, Germany ≥7.5m/pixel Multiband imaging, 380 - 1080 nm Icy moon geology Io activity monitoring and other moons observations Jovian atmosphere dynamics | SWI: Sub-mm Wave Instrument PI: Paul Hartogh, MPS, Germany 600 GHz Jovian Stratosphere Moon atmosphere Atmospheric isotopes
MAJIS: Imaging VIS-NIR/IR Spectrograph PI: Yves Langevin, IAS, France Co-PI: Guiseppe Piccioni, INAF, Italy 0.9-1.9 µm and 1.5-5.7 µm ≥62.5 m/pixel Surface composition Jovian atmosphere | GALA: Laser Altimeter PI: Hauke Hussmann, DLR, Germany ≥40 m spot size ≥0.1 m accuracy Shape and rotational state Tidal deformation Slopes, roughness, albedo
UVS: UV Imaging Spectrograph PI: Randy Gladstone, SwRI, USA 55-210 nm 0.04˚-0.16˚ Aurora and Airglow Surface albedos Stellar and Solar Occultation | RIME: Ice Penetrating Radar PI: Lorenzo Bruzzone, Trento, Italy Co-PI: Jeff Plaut, JPL, USA 9 MHz Penetration ~9 km Vertical resolution 30 m Subsurface investigations

## Slide 20: JUICE Model Payload
JUICE
JMAG: JUICE Magnetometer PI: Michele Dougherty, Imperial, UK Dual Fluxgate and Scalar mag ±8000 nT range, 0.2 nT accuracy Moon interior through induction Dynamical plasma processes | 3GM: Gravity, Geophysics, Galilean Moons PI: Luciano Iess, Rome, Italy Co-PI: David J. Stevenson, CalTech, USA Ranging by radio tracking 2 µm/s range rate 20 cm range accuracy Gravity fields and tidal deformation
PEP: Particle Environment Package PI: Stas Barabash, IRF-K, Sweden Co-PI: Peter Wurz, UBe, Switzerland Six sensor suite Ions, electrons, neutral gas (in-situ) Remote ENA imaging of plasma and torus | PRIDE: Planetary Radio Interferometer & Doppler Experiment PI: Leonid Gurvits, JIVE, EU/The Netherlands S/C state vector Ephemerides bi-static and radio occultation experiments
RPWI: Radio and Plasma Wave Investigation PI: Jan-Erik Wahlund, IRF-U, Sweden Langmuir Probes Search Coil Magnetometer Tri-axial dipole antenna E and B-fields Ion, electron and charged dust parameters | 
JUICE Payload

## Slide 21
JUICE Spacecraft
Prime industrial Contractor: Airbus Defence & Space (Toulouse, France), selected in July 2015
Spacecraft:
  3-axis stabilised
  Mass:
    Launch mass: 5264 kg
    Instruments: 219 kg
    Propellant: 2857 kg
  Solar array 97 m2 ((( ~850 W at Jupiter)
  Fixed High Gain Antenna (X, Ka Bands)
  Steerable Medium Gain Antenna (X, Ka Bands)
  Data Volume ~ 1.4 Gb per day
Notes: 21

## Slide 22
Courtesy Airbus D&S
JUICE Spacecraft
Notes: 22

## Slide 23
Overall Mission Profile
Launch | May/June 2022
Interplanetary transfer (Earth-Venus-Earth-Mars-Earth) | 7.6 years
Jupiter orbit insertion | October 2029
2 Europa flybys | October 2030
Jupiter high-latitude phase | Dec 2030-May 2031
Transfer to Ganymede | June 2031-July 2032
Ganymede orbit insertion | August 2032
Ganymede elliptical orbit/5000 km circular orbit | August-Dec 2032
Ganymede 500 km Circular Orbit | January-June 2033
End of mission | June 2033
Notes: 23

## Slide 24
Cruise Phase with 5 Planetary Flybys

## Slide 25
Jupiter Orbit Insertion

## Slide 26
Science Phases: Distances to Jupiter

## Slide 27
Science Phases: Orbit Inclination

## Slide 28
Icy Moon Flybys
2 EUROPA @ 400 km
11 GANYMEDE @ 400-33 000 km
13 CALLISTO @ 200-6000 km

## Slide 29
GEO
GCO5000
GEO
GCO500

## Slide 30: Challenges
Large mission, large teams
Long cruise phase
Complex navigation in the Jupiter system
Radiation environment
Power and thermal (cold)
Spacecraft electromagnetic cleanliness
Broad science
(relatively low) data rate

## Slide 31
Topics:
Interior
Subsurface
Geology
Atmosphere
Plasma
Planet, moons, rings
Habitability
Link to exoplanets
Jupiter system: largest planet, largest storm, fastest rotation, largest magnetic field, largest moon, largest moon system, most active moons

## Slide 32
Thank you for your attention