## Slide 1: The CAMSS Meteoroid Elemental Abundance Application and Modeling Development
Pete Gural1
Peter Jenniskens2
Melissa Hannan2
1 Gural Software Development; 2 SETI Institute
Meteoroids 2016, June 6-10

## Slide 2
Cameras for All-sky Meteor Surveillance Spectroscopy
CAMSS
Purpose is to obtain meteoroid elemental abundances
  Both relative ratios and absolute #atoms
Sample across a diverse set of comets and asteroids
  Measure Mg, Fe, Na as well as other elemental species
Scale up the number of high resolution spectra obtained
  All sky coverage with year round collection
  16 Objective grating cameras with 0.6 nm/pixel resolution
Automate the labor intensive spectral analysis process
Requires an Integrated Suite of Hardware & Software Tools

## Slide 3
CAMSS Collection System
Operating in Sunnyvale, CA every clear night since April 2013
Over 1000 spectra ready to be analyzed
1379 grooves/mm
Pentax 12mm f/1.2
Watec 902H2 Ultimate
0.6 nm / pixel 1st order
0.3 nm / pixel 2nd order
HP i7-3770 Quad-core
w/16 channel capture/detect/store

## Slide 4
Software Tools and Applications
CAMS - Atmospheric Track and Keplerian Elements
  Capture, Compress, Detect, Calibrate, Coincidence, Trajectory, Orbit
CAMSS - Spectral Analysis
  Responsivity and Extinction calibrations
  Space-time coincidence relative to CAMS derived trajectory
    Spectra extraction, Element selection/fitting, Parameter tuning
    Abundance ratios and atom number density
Software development complete  Ready to process spectra
Spectral Capture
Detection
Sensor Cal
Responsivity
Trajectory
Elemental
Abundances
CAMS
CAMSS
Orbit
Space-Time
Coincidence
q e i W w
Spectral
Model Fitting
Column
Densities
Astrometric
Calibration
Atmospheric Cal Extinction

## Slide 5
Calibration: Responsivity of the Camera System
TBD: Planet or
Iridium Flare
Captured Star Spectrum
Catalog Star Spectrum
1st Order Responsivity
Lab Measured Responsivity
Arcturus mv = -0.1
Response(l) = { Sstar_rows [ StarPix(r,c(l)) – Backgnd(r,c) ] / Vignetting(r,c) }
/ StarSpectrum(l) / ExtinctionApprox(l) = ADU * m2 * nm / Watt / Dlpixel
Airmass < 1.5
Adjust Grating Roll and Yaw
Star Spectrum Provides Response
Lab used as an Optional Response
1st Order
2nd Order

## Slide 6
Calibration: Extinction and Vignetting
Vignetting correction is
applied in focal plane space
Image / cos4 ( 0.095°/pixel * r )
Extinction(l) = AScale * exp{ - AR tR - AO2 tO2 - AO3 tO3 - AD tD - AW tW }
Watec 902H2 w/12mm f/1.2
Use star spectra for any air mass
Average over multiple stars/days
Extinction model fit components:
Rayleigh
O2
Ozone
Dust
Water
t* ≡ Optical Depth at l
O2
O2

## Slide 7
Meteor Modeling Assumptions
Nominal Hot
10,000° K
Nominal Warm
4500° K
Nominal Hot/Warm Volume Ratio = 10-4
MODEL
METEOR
Hot Shock
Warm Wake
Assume Element’s Abundance
is the same in both
Hot and Warm regions
Optically Thin Warm Plasma
Column Density of Ions (or Neutrals) via Saha
Assumes thermodynamic equilibrium
Use fit elements + cosmic abundances  nelectron via iteration on warm neutrals
Optically Thin Hot Plasma
Electron density nelectron via Jones
Assumes electron loss only from 1st air collision
Provides first guess for iterative nelectron
NIon/NNeutral = Saha[ ne, Twarm, IonEnergy(eNeutral, Twarm),
PartFunc(eNeutral, Twarm),
        PartFunc(eIon, Twarm) ]
NIon / NNeutral = bJones, Neutral / ( 1 – bJones, Neutral )
b = x / ( 1 + x ) x = c(e) [ V – Vo(e) ]2 V 0.8
HTW = N(eatom , Thot) / N(eatom , Twarm)
Plasma Radius

## Slide 8
SP_Coincidence Interactive View
Warm / Hot / Neutral / Ion
Responsivity / Extinction
Measured Spectrum
Model Spectrum
350-660 nm
640-950 nm
Emission Line Fiducials
1st and 2nd order
Element Selection
Selection: Column Density, Hot/Warm, Xair
Hb, Htie, He, Grating Roll, Pitch, Yaw
Lines/mm, Line width, Twarm, Thot
Imagery:
Single-frame, Multi-frame, Movie
CAMSS ↔ CAMS Coincidence Info

## Slide 9
Work Flow: Trajectory and Spectrum Coincidence
Tie Spectrum Time Slice to Trajectory Hframe
For frame-by-frame abundance vs height
Define Spectral Hbeg and Hend
For multi-frame integrated spectrum limits
[3] Geometrically feasible to be within grating camera FOV in
1st or 2nd order wavelengths
[1] Trajectory obtained from standard CAMS processing on ALL cameras
[2] Temporally meteor must be within clock synchronization


Grating Camera
fbeg, lbeg
fend, lend
hend
hbeg
V
fcam, lcam

## Slide 10
Work Flow: Select Element and Fit Model Spectrum
Adjust Grating Pitch, Lines/mm, Select Reference Element (e.g. Na), Auto Fit
Adjust Line Width (PSF s), Adjust Column Density
SpectralFlux(l) = N(e) * Selines { 1/s√(2p) } * exp{ - ( l(e)line – l )2 / 2 s2 } * { p PlasmaRadius2 / Range2 }
* { 2 p h e2 / eo me l3 } * gf(e) * exp{ – Eup(e)line / kT } / U(e,T) = Watts / m2 / nm
e ≡ Element’s Neutral or Ion N(e) ≡ Column Density = # / m2 T ≡ Twarm or Thot
1st Order

## Slide 11
Work Flow: Add Additional Elements, Molecules
Add Element (e.g. Mg), Cosmic Abundance for Initial Flux, Adjust Column Density
nelectrons = 6.9e+14 NNa = 3.6e+8 NMg = 3.0e+10 Na / Mg = 1.2%

## Slide 12
Work Flow: Examine Neutrals & Ions, Warm & Hot
Adjust Twarm, Thot, Hot/Warm Volume Ratio, and Column Densities
Twarm = 5700° K
Twarm = 4500° K
Twarm = 3300° K
Focal Plane Image

## Slide 13
Work Flow: Frame-by-Frame Abundance Adjustment
Re-Adjust Column Densities per Element, per Frame
Column Density “N”  Number Density “n”  #atoms per element
1.6 %
1.5 %
1.4 %
1.0 %
1.2 %
Na / Mg

## Slide 14
Next Steps
Begin analysis of the 1000+ spectra
Modify procedures as we process a variety of spectral cases
Solicit feedback on meteor emission modeling