## Slide 1
JWST Imaging
M. Robberto
JWST/NIRCam Team Lead - STScI

## Slide 2
Direct Imaging
High Contrast Imaging: Aperture Mask Interferometry
High Contrast Imaging: Coronography

## Slide 4: Field of View of JWST Instruments

## Slide 5: Imaging Modes

## Slide 6: Outline
Instrument overviews
Dither patterns
Readout Patterns
Sensitivities
Subarrays
Parallel Observations

## Slide 7
NIRCam Terminology
Two fully redundant MODULES A/B mated to opposite sides of optical bench, each 2.2 x 2.2 arcmin2 field of view (FOV) separated by 44”
Each module has one SW CHANNEL (0.6-2.3 μm) and one LW CHANNEL and one LW (2.4-5.0 μm) channel that have the same 2 x 2 arcmin2 FOV
Each SW channel has four 20482 pixel SENSOR-CHIP ASSEMBLIES (SCAs) separated by 5 arcsec;
Each LW channel has one 20482 pixel SCA
        10 DETECTORS TOTAL

## Slide 8: Two Modules x Two channels
Two adjacent fields of view (2.2 arcminute)2 Both fields in SW and LW bands
Two back-to-back modules
5”
5” {
} 40”
}
132”
Notes: WFC3-IR is 123”x136”
Imagine a WFC3 image with 5”/0.13=40 pixels gap between quadrants.

## Slide 9: NIRCam Field of View
Notes: NIRCam's 2 modules operate in parallel to observe a 9.7 arcmin² field of view consisting of two 2.2' × 2.2' fields separated by a ~44" gap. Gaps of ~5" also separate the 4 detectors in each short wavelength module. If full-field imaging is not required, individual modules or smaller subarrays may be used to increase readout speeds and reduce data volumes. To cover larger areas, mosaics are best obtained in combination with primary dithers.

## Slide 10
Vital Statistics
Notes: Field distorsion < 2%

## Slide 11
Passbands and Throughput

## Slide 12: HUDF: WFC3/IR vs NIRCam

## Slide 13: NIRISS
Field of View: 2.2’x2.2’
Plate Scale: 65 mas/pix
Nyquist Sampled at 4 μm

## Slide 14: MIRI
(Looking down from M2)
Notes: Medium Chief Ray coordinates, centered on the middle of NIRCam.

## Slide 16: MIRI
Field of View: 74”x113”
Plate Scale: 110 mas/pix
Nyquist Sampled at 7 μm

## Slide 17: NIRCam imaging
Select Module:
  ALL, [A], B
Select Subarray
  FULL, SUB64P, SUB160, SUB160P, SUB320, SUB400P, SUB640
Select Dither Pattern
Select Filter Pair
  Readout pattern
  Number of groups
  Number of integrations
Operational ordering for dithers, filter changes, and mosaics

## Slide 18: Dithers and Mosaics
Primary Dithers
  FULL
  INTRAMODULE
  INTRASCA
Subpixel
Small-grid
Mosaics
Pre-Canned menu
No filter change
User defined
Filter can be changed

## Slide 19: NIRCam Primary Dithers
The NIRCam primary dither patterns were designed for three general sizes of targets:
  FULL: Large fields without gaps, including mosaics (tiled pointings) of larger areas
  INTRAMODULE: Objects smaller than the individual modules (< 110" across)
  INTRASCA: Objects smaller than the individual SCA detectors (< 50" or < 100" across when optimizing for short or long wavelength observations, respectively)

## Slide 20: FULL Dither Patterns
The NIRCam FULL dither patterns provide full field coverage filling the ~40” gap between modules.
They require multiple guide star acquisitions, increasing overheads on observing time.
FULL dither patterns may be combined to do mosaics of even larger areas.
Notes: FULL 3 and 3TIGHT patterns each include two horizontal shifts of 58" (116" total).
They require at least 1 new guide star (58” is ok at l<30deg)

## Slide 24
3: 18%
2: 71%
1: 11%

## Slide 26
28:1%
29: 6%
30: 23%
31: 38%
32: 25%
33: 7%
34: 1%

## Slide 27: INTRAMODULE Dither Pattern
INTRAMODULE dither fills the 5” SCA gaps, but not the 40” gap between modules.
4x4 grid (up to 16 pointings); 22.5” across
Any number of dither positions between 2 and 16 is allowed.
Only one guide star is required, reducing overheads.

## Slide 28: Intramodule 3
1/3

## Slide 29: Intramodule 16
9/16

## Slide 30: INTRASCA Dither Patterns
INTRASCA dither patterns are designed to observe science targets smaller than ~64”x64” with various parts of a SW detector (SCA) to mitigate flat-field uncertainties.
5x5 grid (up to 25 pointings)
Notes: SMALL ANGLE MANOUVERS <20” take >20”; accuracy 5mas/pixel

## Slide 32: INTRASCA are optimized SW/LW

## Slide 35: NIRCam Subpixel Dithers
Subpixel offsets for image resampling
Intended for accurate photometry, especially
  < 2micron (SW)
  < 4micron (LW)
Steps are integer+fractional pixels (e.g. 2.5 pixels)
Example:

## Slide 36: NIRCam Sub-pixel Dithers

## Slide 37: NIRCAM small-grid dithers
Very SMALL: < 69 mas (~1 FGS pixel)
Very FAST: few seconds
Very PRECISE: ~2 mas/axis
Performed with Fine Steering Mirror (no telescope move)
Optimal for coronographic imaging
Less than ideal for imaging (clusters of bad pixels)

## Slide 38: NIRISS Dithers
NIRISS Imaging is allowed in pure or coordinated parallel mode, since NIRCam is the better choice for all general imaging applications (e.g. bigger field of view, simultaneous blue/red channels, better PSF sampling)
  NIRISS will necessarily follow dither pattern / mosaic strategy of “primary” instrument
  There is no support for the use of subarrays

## Slide 39: MIRI DITHERS
MIRI is undersampled at λ<7micron.
Dithering patterns are designed for PSF oversampling, bad pixel removal and self-calibration.
2-Points
4-Points
Reuleaux
Cycling
limited access options:
Sparse
No Dithering

## Slide 40: 2 point dithers
2 exposures to avoid having the peak of the PSF on the same row or column.
GOALS:
simple background subtraction
minimizes the effects of bad pixels, rows, and columns.

## Slide 41: 4 points dithers

## Slide 42: Reuleaux triangle
12 points
- 3 different sizes (or "scales”):
  Reuleaux Large
  Reuleaux Medium
  Reuleaux Small
Suitable for observing unresolved (or barely resolved) sources.
Medium size Reuleaux pattern on the SUB64 array showing PSF diameters for 6λ/D at 25.5 μm
Medium size Reuleaux pattern on the SUB64 showing PSF diameters for 6λ/D at 7.7 μm
This is the longest wavelength that fits entirely on the SUB64 at 6λ/D.

## Slide 43: Cycling
The Cycling pattern consists of 311 points, randomly drawn from a gaussian distribution
- 3 different sizes (or "scales”): 1) Cycling Large 2) Cycling Medium 3) Cycling Small

## Slide 44: Detectors: NIRCam
Largest defect

## Slide 45: Detectors: Sampling diagram
One Exposure
Two integrations
Three Groups
Four Reads
One Skip

## Slide 47: NIRCam Readout Pattern

## Slide 49: Optimal Readout Patterns

## Slide 50: SCA Performance
CDS noise
CDS noise
Effective
noise
Effective
noise
Notes: NIRCam noise goes from 20 (CDS) to 12 (effective)

## Slide 51
Focal Plane Arrays

## Slide 52: NIRISS Readout

## Slide 54: MIRI Detector performance
Great cosmetics (<300 dead, hot or noisy pixels in the science field).
PSF well described at long wavelengths by the JWST’s diffraction profile.
  At short wavelengths (F560W, F770W filters) a cruciform pattern appears, at a level comparable to the telescope diffraction spikes. Identified with scattering in the detector.
  A model has been developed using PSF and out-of-field straylight test data which predicts that 22% of the point source light at F560W is scattered into the cross (11% for F770W).

## Slide 55: NIRCam Imaging Subarrays
Full Field uses 4 amplifiers, Subarray uses 1
Subarrays are only taken on module B
For imaging subarrays, only SCA B3 for SW
Subarrays have same size in pixels on SW and LW
SW and LW subarrays have the same center on the sky
There are
  Point Source subarrays
  Extended Source subarray

## Slide 56: NIRCam Subarrays

## Slide 57: Subarrays

## Slide 58: MIRI Subarrays
Imager Subarray | Frame time [sec] | Gain in bright source limit
FULL | 2.775 | 1.00
BRIGHTSKY | 0.865 | 3.21
SUB256 | 0.300 | 9.25
SUB128 | 0.119 | 23.32
SUB64 | 0.085 | 32.65
Coronography and time series
Example: SUB128 subarray has a 14” x 14” FoV and can measure point sources through the F1280W filter with fluxes up to 0.027 Jy x 23.32 = 0.6 Jansky without approaching saturation.

## Slide 59
Add 6 mag in
Full-array mode
NIRCam Sensitivity
Notes: Add 256x for full array = 6 magnitudes

## Slide 60: MIRI SENSITIVITY

## Slide 61: MOSAICS
Mosaic patterns (for any instrument) are intended for covering larger areas of the sky than a single field of view.
Fundamental operational difference between Dither and Mosaic:
  Dithers: all spatial positions in a pattern are imaged through the same filter before making a filter change.
  Mosaics: all filters in an observation (and all dithers) are executed before moving to the next mosaic point.
Thus, dithers with large patterns and large step sizes can incur significant overheads due to spacecraft maneuvers.
This must be balanced against lifetime limitations on filter wheel rotations.

## Slide 62: NIRCam MOSAICS
2 rows x 2 columns
306.902" × 133.269" tile spacing
Overlap 0%
row/column shifts: 0/0

## Slide 64: Visit Slew Time

## Slide 65: Coordinated Parallels
Available Cycle 1: • NIRCam Imaging and MIRI Imaging • NIRCam Imaging and NIRISS WFSS
• MIRI Imaging and NIRISS WFSS • NIRCam Imaging and NIRISS Imaging

## Slide 66: Coordinated Parallel Dither Patterns
differences in SI-to-SI orientations and pixel scales
E.g.: MIRI is offset by 4.756 degrees w.r.t. NIRCam
Dither patterns generally keep pixel phases “ideal” to within 0.05 pixel for parallel SI
  • Exception: MIRI at λ > 12 μm (well-sampled anyway)
  • Dither patterns involving MIRI customized for each filter, with offsets >= 3 × FWHMPSF
  • Otherwise typically “Small”, “Medium”, and “Large” dither offsets being offered

## Slide 67: Other imaging modes

## Slide 68: NIRCam Coronagraphy

## Slide 70: Wavefront Sensing

## Slide 71: Questions

## Slide 72
Optical Layout

## Slide 73
NIRCam Pupil and Filter Elements

## Slide 76: Observability Constraints

## Slide 77: Mosaic Group