## Slide 1: Slit Spectroscopy Hands on
Elena Puga, ESA

## Slide 2: NIRSpec and MIRI LRS Slit hands-on
Infrared spectroscopy of Y dwarfs
  NIRSpec
  MIRI LRS
In this hands-on session you will be asked to use:
  The Exposure Time Calculator (ETC) for the NIRSpec fraction
  The Astronomer’s Proposal Tool (APT) for both instruments
The MIRI LRS science case was already part of the ETC hands-on, so that part of the observation planning is assumed to be covered.

## Slide 3: Thinking about strategies

## Slide 4: NIRSpec Subarrays and Readout patterns
Subarray:
  FULL
  Tailored subarrays per individual slit: SUBS200A1, SUBS200A2, SUBS200B1, SUBS400A1
  S1600 subarrays: SUB2048, SUB1024A, SUB1024B, SUB512
  ALLSLITS (S200A1 and S200A2 combined to bridge the detectors gap, but not only. It can also be used to estimate background)
Only traditional readout mode, not the IRS2 noise reduction mode
Readout patterns: NRS and NRSRAPID
Note: maximum exposure duration is 10,000 seconds

## Slide 5: NIRSpec FS detector recommendations
Decision flow to specify detector parameters for a FS observation:
Lower limit
Saturation
Data volume

## Slide 6: MIRI LRS Subarrays and Readout patterns
Subarray:
  FULL (slit)
  SLITLESSPRISM (slitless for Time Series Observations - TSO)
Readout patterns:
  SLOW ( t1=23.890 s)
  FAST ( t1=2.775 s).
    In slitless mode, only FAST mode is allowed.
  where t1 is the resulting group time.
The maximum exposure duration for a single exposure with the LRS slit is 10,000 s.
LRS slit and slitless spectra positions on MIRI imager focal plane

## Slide 7: Background removal strategies
Pixel-to-pixel subtraction
  Compact sources: using nodding
  Extended sources: associated dedicated ″blank sky″ observation at off-scene position
    for NIRSpec: performed only if grating wheel has not moved between the target and off-scene exposures
Master background subtraction
  Standard for extended sources
  created from:
    associated exposure, creating an independently flux-calibrated 1D background spectrum
    list of background elements (like off-source pixels)
  for NIRSpec: is set by pipeline processing if the grating wheel has moved
In ETC, FS nod/dithers are accounted for at detector level, setting the number of exposures.
APT: Dedicated observations for background must be linked to science observations in order to create an association list. This is defined at Target Level in APT. Necessary for pipeline processing flow.
    APT: If the background signal is time variable throughout the year, dedicated “blank-sky” observations should be scheduled consecutively to ensure pixel-to-pixel subtraction. Special requirements: Non-interruptible

## Slide 8: NIRSpec Nods and dithers
Nods: offsets that produce data to be subtracted in pipeline processing, in order to cancel in-field background flux. Nod options are typically best used for targets that are not significantly spatially extended. (2, 3, or 5 points), depending on the number of exposures needed/possible.
Dithers: offsets of the target position over multiple exposures, to even out or mitigate detector effects, help remove cosmic rays, improve spatial sampling, and increase signal-to-noise and flux accuracy.
APT
      Primary dithers: nod along the slit used to subtract background flux. Recommended 3, 5.
      Sub-pixel dithers: to improve spatial and/or spectral pixel sampling, only in addition to Primary Dither pattern for point sources. Not recommended in spectral dimension.
      Across gap SAM. Offset executed by selecting the option “S200A1 and S200A2” only in the high resolution gratings

## Slide 9: NIRSpec Nods and dithers
Decision tree for choosing the right nod/dither pattern for FS observations based on the source compactess.

## Slide 10: MIRI LRS Nods and dithers
For MIRI, dithering is required to achieve accurate photometry and to provide superior sampling (Gordon et al. 2015)
LRS slit dithers (for slitless mode, dithering is not allowed):
  ALONG SLIT NOD (default for compact sources) uses a 2-point "nod" where a point source is dithered between positions that are located approximately 30% and 70% of the way along the slit length.
  MAPPING customizable offsets along-slit and across-slit. It is recommend that the chosen step sizes are smaller than, or on the order of the slit size (approx. 4.7 x 0.5"). Extended sources mapping can also be produced by mosaicing. Recommended dither steps of 1” in both directions. A dedicated background observation may be needed.
  NONE (only permitted for SLITLESSPRISM)
Dithers ALONG SLIT NOD Layout on the LRS slit

## Slide 11: NIRSpec FS Target Acquisition
FS TA methods:
  WATA (recommended) using science or offset target centred in S1600A1. 11-18 minutes. Expected accuracy: 20 mas, and depends on centroiding accuracy of the target (ephemeris).
  MSATA requires defining 5-8 reference stars (may require pre-imaging). It is specified at the visit level of the observation, not directly at the observation template. 24-30 minutes. Expected accuracy: 20 – 25 mas (optimal), <50 mas (relaxed), depending on the catalogue relative accuracy.
  NONE is not recommended for FS. The resulting pointing accuracy will be that delivered by the GS acquisition at the start of the observation. For reference, the absolute pointing performance of JWST for NIRSpec is expected to be 100 mas
Strategies and parameters:
  WATA:
    Subarray configurations: SUB32, SUB2038, FULL (increasing frame time)
  MSATA:
    Subarray configuration: FULL
  Filters: F110W, F140X, CLEAR
  Readout pattern: NRSRAPID, NRSRAPIDD1, NRSRAPIDD2, NRSRAPIDD6
  Groups/Integrations are fixed
  TA readout mode switch with respect to science parameters costs extra in time.

## Slide 12: MIRI LRS Target Acquisition
TA procedure:
  LRS slit mode
Use of science or offset target at distance <60 arcseconds
TA is NOT mandatory in the LRS slit APT template; however, for observations of point or compact sources it is highly recommended.
Strategies and parameters
  Filters: F560W, F1000W, F1500W, and FND
  Subarray configuration: N/A, controlled by the subarray science parameter
  Readout patterns: FAST(default), FASTGRPAVG, FASTGRPAVG8, FASTGRPAVG16, FASTGRPAVG32, FASTGRPAVG64
  Groups are selectable but fixed (4, 6, 8, 10), integrations is always 1
The user should always refer to the ETC for signal-to-noise calculations.

## Slide 13: Science case

## Slide 14: Science Overview
Goal
  To obtain spectroscopic observations of a Y dwarf across the entire JWST NIRSpec and MIRI LRS wavelength ranges to understand whether these atmospheres are shaped by chemical disequilibrium driven by vertical transport or the formation of water clouds, and constrain the object’s gravity, hence mass.

## Slide 15: Observations Methodology
Methodology
  Compare high-quality low and medium resolution Infrared spectra from 0.6 to 13 microns, to models of cool atmospheres at different temperatures, gravity, degrees of turbulence, chemical equilibrium or disequilibrium driven by vertical transport, and clouds.
Planned observations
  NIRSpec fixed slit spectroscopy
  MIRI LRS slit spectroscopy
Source Type
  Point source
Observation strategy
  PRISM and G395M dispersers for NIRSpec to obtain R~100 and R~1000, respectively and MIRI LRS R~100
  3-point nod NIRSpec / 2-point nod MIRI
  TA on science source

## Slide 16: Getting started ETC NIRSpec WB ID: 30896 MIRI LRS WB ID: 30989

## Slide 17: Scenes and Sources
NIRSpec:
  1 source with user supplied model spectrum morley_spec_ETC_noscale.txt renormalized to measured Vega magnitudes HST/WFC3 F140X.
MIRI
  Workbook: 30989

## Slide 18: Calculations
Overview

## Slide 19: NIRSpec Calculation for Target Acquisition
WATA in ETC is available.

## Slide 20: Getting started APT

## Slide 21: Cheat APT screenshots…

## Slide 22: APT Fixed-slit spectroscopy templates
When creating a new observation, the user defines the APT template
APT fixed-slit spectroscopy templates are divided into four sections:
  Generic information
  Observation information
  Target acquisition parameters
  Science parameters

## Slide 23: APT Fixed slit spectroscopy template
NIRSpec
Generic information
Observation information

## Slide 24: APT Fixed slit spectroscopy template
NIRSpec

## Slide 25: APT Fixed slit spectroscopy template
MIRI

## Slide 26: Further reading

## Slide 27: Slit Help and JDOX
Detector Strategies
  NIRSpec detector recommended strategies
NODS and Dithers
  NIRSpec Background Recommended Strategies
  MIRI LRS Recommended Strategies – Background observations
  NIRSpec Dithering Recommended Strategies - FS
  MIRI LRS Dithering Recommended Strategies
Target Acquisition
  NIRSpec Target Acquisition Recommended Strategies
  MIRI Target Acquisition Generic Recommended Strategies
  MIRI LRS Target Acquisition Recommended Strategies