## Slide 1: MOS hands-on
Tim Rawle, ESA

## Slide 2: NIRSpec MOS hands-on
Multi-object spectroscopy of distant galaxies
In this hands-on session you will be asked to use
  The Astronomer’s Proposal Tool (APT)
  More specifically, the MOS Planning Tool (MPT) which is part of the APT
The same science case was already part of the ETC hands-on, so much of the observation planning is assumed to have been completed

## Slide 3: Thinking about strategies - recap

## Slide 4: Shutter planning constraints
Slit loss is a function of the relative location in the shutter
MPT allows adjustment of the constraint on where sources can be placed in shutters
 | Unconstrained (source may be behind the bar) | Entire open shutter area (default) | Midpoint | Constrained | Tightly constrained
Minimum relative flux transmission at 2.95μm | 12% | 30% | 62% | 75% | 85%

## Slide 5: Nodding
Open slitlets in cross-dispersion direction
There are four selectable slitlets in MPT: 1, 2, 3, 5
Telescope is repositioned slightly between exposures
  No MSA re-configuration
  Background subtraction between nodded exposures
  Improves PSF sampling and bad pixel mitigation
The spectrum from a slitlet will be segmented, with bar shadows between the individual shutters

## Slide 6: Dithering (fixed dither)
Telescope repointed and MSA re-configured so many of the same sources fall in different shutters
  Can be used to cover the wavelength gap
  Improves PSF sampling and mitigates bad pixels
  Allows observation of additional sources e.g. those behind shutter bars or the MSA mounting plate
  Can mitigate effects of light leakage through MSA
During optimisation, MPT will attempt to observe as many sources as possible at all dithers
Nodding and dithering can be used alone or together

## Slide 7: Target acquisition
MSATA is expected to be the usual TA method for the MOS
  uses 5-8 reference stars over the entire MSA FoV
  8 chosen as a trade-off between TA accuracy and overheads
MPT used to select reference stars at the assigned APA that will not be behind MSA bars or in failed shutters. This vetting is done at the Visit level at the first pointing in the Visit

## Slide 8: Pre-imaging with NIRCam
Is imaging available with
  deep enough to identify sources?
  wide enough to fill the MSA and plan reference stars?
  accurate enough astrometry to plan MOS?
If not, request NIRCam pre-imaging in your proposal
  accurate enough astrometry to plan MOS?
  NIRCam image should be large enough to allow for any NIRSpec APA
    Ideally 5x5 arcmin
    typically a 2x1 mosaic + dithers to cover gaps
  NIRCam observations must be flight ready at proposal submission

## Slide 9: The science case

## Slide 10: Science overview
Goal
  This program aims to study the evolution of galaxies from the early Universe (z>10), through the end of the dark ages (z=7-9), to the epoch of galaxy assembly (z=2-6)
    Understanding very early stages of galaxy formation
    Probing the epoch of re-ionization and the role of galaxies
    Constraining the build-up of stellar mass and metals through time
    Understanding the role of AGNs.
    And looking for surprises…

## Slide 11: Observation methodology
Methodology
  An in-depth program of this type would typically combine deep imaging (NIRCam) and follow-up spectroscopy (NIRSpec MOS)
  In the following, we will use a much simpler example:
    deep NIRSpec MOS observations at a single location
    input source catalog derived from existing HST imaging
Spectral configuration
  MOS at low and medium spectral resolution
Type of sources
  Galaxies over a wide range of redshifts handled as compact (point-like) objects
Observation strategy
  Combination of nodding (1x3 slitlets) and dithering

## Slide 12: Instrument configuration
Low spectral resolution (CLEAR/PRISM)
  sensitivity to continuum
  wavelength coverage (0.6-5.3 μm at once)
  higher-multiplex MOS thanks to the shorter spectra on the detector
  Main drawback: lack of spectral resolution…
Medium spectral resolution (F100LP/G140M, F170LP/G235M, F290LP/G395M)
  clean separation of emission lines
  allows accurate centroid calculation for the lines
  Main drawback(s):
    3 configurations required to cover 1.0-5.2 μm
    high multiplex only possible if spectra allowed to overlap
Configurations give complementary information: include all 4

## Slide 13: Getting started

## Slide 14: Getting started
Follow the steps on the handout
  Plan your observation strategy
  Open APT
  Load the catalogue
  Set-up the MPT Planner
  Generate the plan
  Create the observation

## Slide 15: Cheat screenshots…

## Slide 16: Plan your observation
NOTE: for simplicity, create a program with 27 exposures per medium-resolution grating
Dither | Nod | CLEAR/PRISM | F100LP/G140M | F170LP/G235M | F290LP/G395M
1 | 1 | 8 | 3 | 3 | 3
 | 2 | 8 | 3 | 3 | 3
 | 3 | 8 | 3 | 3 | 3
2 | 1 | 8 | 3 | 3 | 3
 | 2 | 8 | 3 | 3 | 3
 | 3 | 8 | 3 | 3 | 3
3 | 1 | 8 | 2 | 2 | 2
 | 2 | 8 | 2 | 2 | 2
 | 3 | 8 | 2 | 2 | 2
TOTAL Exps |  | 72 | 24 | 24 | 24

## Slide 17: Open APT

## Slide 18: Load the catalogue

## Slide 19: Set-up the MPT planner

## Slide 20: Planner parameters

## Slide 21: Create the observation

## Slide 22: Further reading

## Slide 23: MOS/MPT Help and JDox
JWST Help Desk: https://jwsthelp.stsci.edu
JDox Home page: https://jwst-docs.stsci.edu/
  Updated for the new version of APT/MPT
Specific MOS/MPT materials:
  MOS Roadmap
  Multi-Object Spectroscopy
  NIRSpec MOS Observing Process
  NIRSpec MOS Operations
    Catalogues and Images
    Pre-Imaging Using NIRCam
    Confirmation Images
    Slit Losses
  NIRSpec MOS Recommended Strategies
  MOS APT Template