## Slide 1: Time Series Observations: Hands-on
Stephan Birkmann, ESA

## Slide 2: Time Series Observations
30 min (including 15 min of “hands-on” exercises)

## Slide 3: Time Series Observations (TSOs) – Examples
Transiting exoplanets
Animation: Jason Eastman
Stellar variability
Animation: Benjamin Rackham
Supernovae
Animation: N. Johnston/Supernova Cosmology Project

## Slide 4: Example: Transiting Exoplanets as TSO Targets

## Slide 5: What Is Special About TSOs?
Usually relative measurements aiming at high precision
  Requires stability of observatory, instruments, and detectors; no dithers, exclusive use of instrument (no parallels), no detector reconfigurations / transitions while taking data
Supports long (>10,000 s) exposures with many (usually short) integrations
  Allows for continuous/uninterrupted and stable observations of events from a few hours (e.g. exoplanet transits) to days (e.g. phase curves)
  Exposures continue through High Gain Antenna moves
Often have stringent timing requirements on scheduling/start of observation (we want to see the transit / eclipse)
  Needs special requirement(s) in APT
  Might result in scheduling overhead (for observations with start window constrained to less than 1 hour) -> avoid if possible (increase baseline instead)

## Slide 6: TSOs and JWST – Observing Modes
Spectroscopy
Photometry

## Slide 7: Selection of Instrument / Mode to Use
Desired (spectral) coverage/range
  What (spectral) features are important for your science case?
Desired spectral resolution
  SNR can be improved by spectrally binning data at cost of resolution
Source brightness / saturation limits
Other concerns / limitations
  Slitless vs. “large” slit
  Possible contamination from nearby sources (in particular for slitless observations)

## Slide 8: Preparing for Time Series Observations
As with most other observations there are three basic steps preparing TSOs:
Assess target observability given JWST LoS and target timing constraints. Check for possible target contamination when using slitless spectroscopy. Useful tools include: JWST GTVT, ExoCTK
Assess feasibility of observations and select the best observing mode/instrument for your science case. Useful tools include: PandExo, JWST ETC, ExoCTK
Create observations in APT. Remember to provide special timing requirements if needed (e.g. for transit observations):
  Zero phase
  Period
  Phase range for start of observations

## Slide 9: Exercise 1 – Observability using ExoCTK
Go to exoctk.stsci.edu
Under Observation Planning, select “Contamination Overlap” (yes, that’s right)

## Slide 10: Exercise 1 – Observability using ExoCTK
Go to exoctk.stsci.edu
Under “Observation Planning”, select “Contamination Overlap” (yes, that’s right)
Type in target name to resolve or provide target coordinates
Select instrument (only affects reported PA)
Click “Calculate Visibility” or “Calculate Visibility and Contamination” (available for NIRISS SOSS and NIRCam Grism Spectroscopy only)

## Slide 11: Exercise 1 – Observability using ExoCTK
Go to exoctk.stsci.edu
Under “Observation Planning”, select “Contamination Overlap” (yes, that’s right)
Type in target name to resolve or provide target coordinates
Select instrument
Click “Calculate Visibility” or “Calculate Visibility and Contamination”
Inspect target visibility (and contamination if applicable)

## Slide 12: Exercise 2 – Exposure Settings and More
Use JWST ETC and/or ExoCTK and/or PandExo to estimate best exposure parameters
How long should your transit observations be? According to JDox:
This might seem long, but accounts for possible detector transients at beginning of exposure(s), uncertainty in transit times, etc. Justify if you go shorter (or even longer)
  Do not go below 2 T14 = ½ T14 + T14 + ½ T14 (unless you have a very compelling reason to do so)
  Keep in mind phase start/end special requirement; recommendation is to keep phase window at least 1 hour wide, in order to prevent direct scheduling overhead (of 1 h)
T14
0.75 + max(1 hr, T14/2)
max(1 hr, T14/2) + 1 hr

## Slide 13: Exercise 2 – Exposure Settings and More
Go to exoctk.stsci.edu and select “PandExo” from the top menu bar
  Select “JWST”
  Select “New Calculation”

## Slide 14: Exercise 2 – Exposure Settings and More
Go to exoctk.stsci.edu and select “PandExo” from the top menu bar
  Select “JWST”
  Select “New Calculation”
Fill out values for star and planet
  properties
  Can use defaults for many known systems
Fill out ”Baseline” duration number
  of observed transits
  Remember recommendation for
    total observation duration here:
    0.75 h + max(1 h, T14/2) + T14 + max(1 h, T14/2) + 1 h
    = 4.91 h

## Slide 15: Exercise 2 – Exposure Settings and More
Fill out instrument setup and assumed
  noise model
  Use “optimize” for # of groups if you want PandExo to estimate for you
  Specify target counts/charge (typically 80% full well for NIR and 50% for MIR instrument(s))
Click “Submit” and simulation will run
Click on “eye” symbol to expect
  results

## Slide 16: Exercise 2 – Exposure Settings and More
Inspect simulated results

## Slide 17: Exercise 2 – Exposure Settings and More
“Timing Info” is useful to set exposure parameters (groups & integrations for selected subarray)
  Use in APT
Inspect Warnings
  “All good”: no issues with the simulated observation
  Otherwise assess if change of mode and/or instrument is warranted

## Slide 18: Putting It Into APT
Input target(s) and select chosen Instrument/Observing Template
Target Acquisition:
  Recommended to do TA (known and consistent source placement)
  Some targets will be too bright to acquire directly (in particular for NIRSpec); APT allows user to select nearby TA reference target
  Estimate TA parameters using the ETC (like for any other TA)
Exposure setup / duration / number of groups per integration / etc.:
  Use results from JWST ETC or PandExo
Special requirements:
  Time Series Observation (implicit in some templates)
  No Parallels
  Phase (Phase range, Period, Zero phase)
    Keep in mind direct scheduling overhead of 1 hour if the specified phase range corresponds to less than 1 hour
    Can also the ExoCTK phase constraint calculator (does not yet follow recommended baseline)

## Slide 19: Putting It Into APT
NIRISS example
NIRSpec TA on
reference target
Special requirements on timing

## Slide 20: Summary & Reminders
Always check the JWST Documentation:
jwst-docs.stsci.edu
(includes the call for proposals for cycle1
and many use cases and examples)
Questions? Cannot find the answer? Contact the JWST Help Desk:
jwsthelp.stsci.edu
Assess target observability given JWST and target timing constraints. Useful tools include: JWST GTVT, ExoCTK
Select the best observing mode / instrument for your science case. Useful tools include: PandExo, JWST ETC, ExoCTK
Create observations in APT. Remember to provide special timing requirements if needed (e.g. for transit observations)