## Slide 1
NIRCam Imaging
M. Robberto - STScI

## Slide 2
NIRCam Basics
NIRCam is JWST’s primary visible and near-IR wavelength imager
NIRCam offers low-resolution grism spectroscopy and Lyot coronagraphy
NIRCam is JWST monitor of OTE wavefront error
Two fully redundant MODULES A/B mated to opposite sides of optical bench, each 2.2 x 2.2 arcmin2 field of view (FOV) separated by 44”
Each module has one SW CHANNEL (0.6-2.3 μm) and one LW CHANNEL and one LW (2.4-5.0 μm) channel that have the same 2 x 2 arcmin2 FOV
SW channel has four 20482 pixel SENSOR-CHIP ASSEMBLIES (SCAs) separated by 5 arcsec; LW has one 20482 pixel SCA

## Slide 3
NIRCam
NIRCam in ISIM

## Slide 4: Field of View of JWST Instruments

## Slide 5
Optical Layout

## Slide 6: NIRCam Field of View
Notes: NIRCam's 2 modules operate in parallel to observe a 9.7 arcmin² field of view consisting of two 2.2' × 2.2' fields separated by a ~44" gap. Gaps of ~5" also separate the 4 detectors in each short wavelength module. If full-field imaging is not required, individual modules or smaller subarrays may be used to increase readout speeds and reduce data volumes. To cover larger areas, mosaics are best obtained in combination with primary dithers.

## Slide 7: Two Imagers in Two Modules
Two adjacent fields of view (2.2 arcminute)2 Both fields in SW and LW bands
Two back-to-back modules
5”
5” {
} 40”
}
132”
Notes: WFC3-IR is 123”x136”
Imagine a WFC3 image with 5”/0.13=40 pixels gap between quadrants.

## Slide 8
Vital Statistics
Notes: Field distorsion < 2%

## Slide 9
NIRCam Pupil and Filter Elements

## Slide 10
Passbands and Throughput

## Slide 12
Add 6 mag in
Full-array mode
Sensitivity Limits
Notes: Add 256x for full array = 6 magnitudes

## Slide 13: NIRCam imaging
Select Module:
  A, B, ALL
Select Subarray
  FULL, SUB64P, SUB160, SUB160P, SUB320, SUB400P, SUB640
Select Dither Pattern
Select Filter Pair
  Readout pattern
  Number of groups
  Number of integrations

## Slide 14: NIRCam Imaging Subarrays
Full Field uses 4 amplifiers, Subarray uses 1
Subarrays are only taken on module B
For imaging subarrays, only SCA B3 for SW
Subarrays have same size in pixels on SW and LW
SW and LW subarrays have the same center on the sky
There are
  Point Source subarrays
  Extended Source subarray

## Slide 16: Subarrays

## Slide 17
Focal Plane Arrays

## Slide 18: Dithers and Mosaics

## Slide 19: NIRCam Primary Dithers and Mosaics
The NIRCam primary dither patterns were designed for three general sizes of targets:
  FULL: Large fields without gaps, including mosaics (tiled pointings) of larger areas
  INTRAMODULE: Objects smaller than the individual modules (< 110" across)
  INTRASCA: Objects smaller than the individual SCA detectors (< 50" or < 100" across when optimizing for short or long wavelength observations, respectively)

## Slide 20: FULL Dither Patterns
The NIRCam FULL dither patterns provide full coverage with no gaps between modules.
They require multiple guide star acquisitions, increasing overheads on observing time.
FULL dither patterns may be combined to do mosaics of even larger areas.

## Slide 24
3:18% - 2:71% - 1:11%

## Slide 26
28:1%
29: 6%
30: 23%
31: 38%
32: 25%
33: 7%
34: 1%

## Slide 28: Observability Constraints

## Slide 29: Mosaic Group

## Slide 30: INTRAMODULE Dither Patterns
INTRAMODULE dithers are smaller, covering the SCA gaps, but not the gap between modules.
Only one guide star is required, reducing overheads.
Any number of dither positions between 2 and 16 is allowed.

## Slide 31: Intramodule 3
1/3

## Slide 32: Intramodule 16
9/16

## Slide 33: INTRASCA Dither Patterns
INTRASCA dither patterns are designed to observe small science targets with various parts of a SW detector (SCA) to mitigate flat field uncertainties.
The science target is considered to be “small", “medium", or “large” if it fills < 25%, 50%, or 75% of the detector, respectively.
Dither step sizes are optimized for either the short or long wavelength channel (SWC or LWC) detectors, with the latter allowing for larger dither steps.

## Slide 37: INTRASCA are optimized SW/LW

## Slide 40: NIRCam Secondary Dithers

## Slide 41: Sampling diagram
One Exposure
Two integrations
Three Groups
Four Reads
One Skip

## Slide 42: NIRCam Readout Pattern

## Slide 44: FPA Performance
CDS noise
CDS noise
Effective
noise
Effective
noise
Notes: NIRCam noise goes from 20 (CDS) to 12 (effective)

## Slide 45: NIRCam Coronagraphy

## Slide 47: Wavefront Sensing

## Slide 48: HUDF: WFC3/IR vs NIRCam