## Slide 1
Niriss SINGLE OBJECT Slitless spectroscopy
Chris Willott, Loic Albert, René Doyon, and the FGS/NIRISS Team
ESAC JWST
27 Sept 2016

## Slide 2: Outline
Grism and spectral traces
Operations concept
Detector sub-arrays and readout modes
Wheel repeatability considerations
Faint and bright limits, example data
Field stars contamination
Spectral orders contamination

## Slide 3: Single Object Slitless Spectroscopy
Uses the GR700XD grism with no filter

## Slide 4: NIRISS GR700XD Grism
λ
15 pixels
CV3 Observed Monochromatic
PSF (1300 nm)
tilt = 0.6°
  Grism with built-in defocussing weak lens to increase dynamic range and minimize systematic noise due to undersampling and flatfield errors.
  Optical implementation to the successful scanning mode used on HST.
99% - 36 pixels

## Slide 5: Spectral Traces on the Detector
Two sub-array choices:
256 x 2048 – all orders
1st: 830 – 2816 nm
2nd: 600 – 1409 nm
96 x 2048 – only 1st order
    Gain 1 magnitude in bright limit
R=500 to 2500

## Slide 6: Operations Concept – Target Acq.
1. Acquisition through the NRM (T=15%) and F480M filter using a 64x64 sub-array (saturating for J<~5).
2. Single pass acquisition with precision of ~1/10 pixel.
3. Grism in. Repeatability of wheel is 0.15 degrees. Baseline is no fine tuning of the trace position.
4. Observing Sequence: A single exposure (FITS file) containing large number of integrations to maximize efficiency. No loss between integrations beside array reset.

## Slide 7: Operations Concept – Contamination
Case of GJ 1214b – Field Orientation.
Contamination can be mitigated
10°
5°
0°
15°
20°
25°
30°
35°
Tool is available to find PAs that minimize contamination

## Slide 8: Operations Concept – Wheel Repeatability
Order 1 Trace Position on the Detector
blue  First Order Trace  red
Spatial Axis Delta - ΔX (pixels)
Dispersion Axis - Y (pixels)
CV3 test moving between CLEARP and GR700XD pupil wheel position
10 repeats per position
Imperfect wheel repeatability introduces a rotation of the spectral traces: θ=tan-1(0.7/2048) = ~0.02 degrees.

## Slide 9: Operations Concept – Detector Readout

## Slide 10: Expected Science Targets
Figure courtesy of George Ricker (TESS PI)
NIRISS Saturation Limit
NIRISS Faint Limit

## Slide 11: Target Faint Limit
2nd Order
4 hr clock time
15 ppm noise floor
Teff = 3200
At full spectral resolution
J=14
J=12
J=10
J=7

## Slide 12: Target Saturation Limits
J | NG | Sub | Coverage | Warnings
>8.0 | 2+ | 256 | full 0.6-2.8 | None
7.25-8.0 | 1 | 256 | full 0.6-2.8 | Bias drift uncertainty
6.75-7.25 | 1 | 256 | full 0.6-2.8 | Sat. pix. in "horns" for λ=0.96-1.46 μm
6.25-6.75 | 1 | 256 | full 0.6-2.8 | Can recover λ<1.40 μm from order 2
5.75-6.25 | 1 | 256 | 0.6-1.4+2.0-2.8 | Order 1 saturated for λ<2.0 μm
>6.0 | 1 | 96 | 1.0-2.8 (order 1) | Bias drift uncertainty
5.5-6.0 | 1 | 96 | 1.0-2.8 (order 1) | Sat. pix. in "horns" for λ=0.96-1.46 μm
<5.5 | 1 | 96 | Less of blue end | λ=1.2μm@5.25, 1.8@4.5, etc
Coverage and Risks at Various Magnitudes

## Slide 13: Simulated Data

## Slide 14: Spectral Order Overlap
96x2048
2nd and 1st orders cross contamination
Requires modeling in spectral extraction

## Slide 15: Summary
NIRISS Single Object Slitless Spectroscopy has excellent capabilties for exoplanet transits:
  Simultaneous coverage from 0.6 to 2.8 microns with most of spectrum at spectral resolution R>1000.
  Slitless design with extended spatial PSF spreading light over more pixels.
  Two sub-arrays and several readout modes matched to target fluxes.
  Stable operation mode of long exposures containing many integrations.
  Simulation tools available at http://jwst.astro.umontreal.ca