## Slide 1
NIRSpec simulation data-package
Giovanna Giardino, Pierre Ferruit, Jacopo Chevallard, Camilla Pacifici
ESAC JWST Workshop

## Slide 2: NIRSpec simulations
Ingredients of the simulation
Simulation procedure
Outline of the data package
MOS simulation & IFS simulation

## Slide 3: Ingredients for the Sky: sources
Mock spectra: z = 4 - 8
BEAGLE
BayEsian Analysis of GaLaxy sEds
Photometry (10 bands - Δλ= 0.4 – 1.6 μm)
MOS simulation - DEEP FIELD
HUBBLE eXDF
(Catalogue Bouwens et al. 2014)
WFC3 Field 2.3'x2.0’ - MOS FOV is 3.4’ x 3.6’
Bouwens Catalogue tiled 2x2
~ 700 objects
~ 2800 objects
Chevallard & Charlot 2016, MNRAS, 462
Notes: BEAGLE: This tool incorporates the consistent modeling of stellar radiation and its transfer through the interstellar and intergalactic media, allowing one to derive “phyiscally” plausible galaxy spectra from photomotric and spectral data, in a Bayesian framework.

## Slide 4: Ingredients for the Sky: background
Zodiacal light (0.5-5.5 μm):
Blue-part: reddened spectrum
of a solar analogue (Phoenix code)
Red-part: Black-Body T=256.15 K
Parasitic light (open telescope!):
“Galactic sky” straylight.
Zodiacal straylight
Emission from telescope
Worse case!

## Slide 5: MPT selection of targets and MSA configuration
2 pointings dither
nod in 1x3 slitlet
6 exposures
Disperser: PRISM

## Slide 6: Procedure
Count rate images – 94.9 ks
100 integrations in IRS2 read-out mode
Include photon noise (incl. dark) + read noise
Instrument Performance Simulator
Radiometric response (throughput, slit- diffraction-losses, QE)
Sky Scene
Sources (pointlike) + Background
Fourier optics software + coordinate transf. closely matching instrument

## Slide 7: Simulated exposure #1

## Slide 8: Background subtracted f = A-0.5(B+C) ~ 100 ks integration
Dither 0

## Slide 9: Background subtracted – 100 ks integration
Dither 1

## Slide 10: Extracted products (NIPS)
Spectral trace (wavelength and spatial coordinate for each pixel)
2D recitified spectra (wavelength - spatial coordinate)
1D spectrrum
FITS files
Uncalibrated flux units
Dorner, Giardino, Ferruit et al. 2016, A&A, 592

## Slide 11: Calibrated spectra
Simulated observation of radiometric standard (1.0 W m-2 m-1)
 Comparison with synthetic input spectra
MAB = 28.4

## Slide 12: Data package MOSsimulationESAC2016
Input catalogue and Spectra
APT file
Count rate observations:
  Background subtracted count-rate images
  (2 files, one for each dither pointing)
  6 Exposures (3 nodding x 2 dithers), noisy and noiseless
Extracted products
  Data files of Traces, 2D rectified spectra, 1D spectra
  (FITS)
  Plots of Traces, 2D rectified spectra, 1D spectra
  (PNG)
 AREDME file

## Slide 13: IFS Simulations –Input data
Input data cube (prepared by C. Pacifici): a z~3 galaxy – fit of the (photometric) HST data of one of the sources in the CANDELS program, using a library of spectral energy distribution models.
GAL2136
F160W filter

## Slide 14: Sky Scene  IPS input

## Slide 15: Simulation output – Count-rate image
11.2 ks - 12 integrations in IRS2 read-out mode
Include photon noise (incl. dark), read noise

## Slide 16: Background subtracted – Count-rate image

## Slide 17: Data package JWST-NIRSpec-IFU-simulations-GAL2136-20160923
 JWST-NIRSpec-IFU-simulations_20160923.pdf

## Slide 18
Enjoy your data tapas!

## Slide 19: MOS Simulations characteristics
Assumptions: point-sources!
Includes:
zodiacal background, galactic + zodiacal parasitic + telescope emission (uniform!)
Fourier wave optics simulation + radiometric propagation (PSF , slit-effect, slit and diffraction loss, instrument throughput - field dependent)
Ideal Noise: photon noise (incl. ideal dark currents) + read noise
Sort-of-cosmetics (TBD with Pierre)
Does not include:
1/f detector noise
Real dark map
Cosmic rays
Other detector effects (IPC, non-linearity)
MSA failed shutters, leakage, finite contrast
Background variations across the field
Calibration errors/noise: e.g. no flat field noise, perfect flux calibration, perfect wavelength calibration for centered source